INSTALLATION INSTRUCTIONS

Thank you for purchasing a Stainless Steel Systems Converter Back Exhaust System.

As Mustang Enthusiasts we design our products with focus on ease of installation, increased power and distinctive sound.  We believe you will find this system to be the best value on the market today which should last the lifetime of your vehicle.

This Stainless Steel Systems Converter Back Exhaust System (SS990433) has been designed for 1999-2004 Ford Mustang equipped with a 4.6L engine.

Please take time and read all instructions prior to installation.  Stainless Steel Systems assumes no responsibility for damages occurring due to improper installation, lack of taking proper safety precautions or poor fit due to other aftermarket parts which may alter fitment.

Installation photographs available online at www.sss-exhaust.com/installss990433.htm.

Tools Required.

- A saw, preferably a reciprocating saw, cutoff wheel, or hack saw.

- 13mm socket or combination wrench

- 14mm socket or combination wrench

- 17mm socket or combination wrench

- Spray Lubricant for loosening bolts.

Parts included

The system is packaged in two separate boxes, one contains the drivers side and one contains the passenger side.

The following contents should be verified in each box prior to installation.

- (#1 pipe)  The flow tube that connects the muffler to the factory H-pipe.

- (#2 pipe)  The muffler.

- (#3 pipe)   Includes two hangers already welded into position.

- (#4 pipe)   Is the first half of the over axle tube.

- (#5 pipe)   Is the rear half of the over axle tube.

- (#6 pipe)   Is the rear tip.

- 8 – 2.5inch band clamps.

- Rear hanger assembly with bracket, hanger, and 3 – 13mm bolts with washers, nuts.

Before Installation

- Remove all pieces from the respective boxes and lay out the system on the ground or table making sure not to scratch the surface of the pipes.

- Carefully inspect all pieces of the system, and compare the parts to the parts list.

- Disconnect negative battery terminal lead.

- Support the vehicle on the appropriate lift, allowing for full extension of the rear axle housing.

- Remove the factory system.  The installer will need to cut the factory pipe after the muffler in order to work the pipes out from over the rear axle housing.  It is at this point the rear housing will need to be fully unloaded.

Installation

- Working with one side at a time, install the #1 pipe to the H-pipe and snug the bolts by hand allowing for full rotation of the #1 pipe.

- Attach the #3 pipe to the factory isolaters/hangers.

  - Use a spray lubricant on the isolators to facilitate easy installation of the hangers.

- Slide a clamp on the back of the #1 pipe and the front of the #3 pipe.

- Install the #2 pipe with the logo facing down (muffler).

- Snug the clamp bolts only enough to keep the 3 pieces together.

- Slide a clamp on the front of the #4 pipe.

  - Install the #4 pipe into the system, place a clamp on the rear of the pipe (don’t snug the rear clamp)

  - Snug the front clamp bolts hand tight only.

- Install the bracket and hanger to the #5 pipe or tip.  Do not tighten clamp bolts at this time, you will need to be able to move these around.

- Install the #5 pipe into the system and place the hanger into the factory isolator/hanger.

- Adjust the system as per your preference.

  - Once adjusted properly, looking for clearance to frame, axle housing, and floor pan, tighten all the clamps completely once satisfied all clearances are sufficient.

- Repeat for the next side.

- Start the car and listen/look for any leaks.

- Re-torque all bolts after initial run in.

- Enjoy.

# Text boxes

Warning:  Stainless Steel Systems recommends that an exhaust shop or professional installer with the correct equipment install all automobile exhaust equipment.

When working on or around any vehicle exercise caution.  Please let the exhaust system fully cool prior to removal.  Please consult the vehicle manual for correct lifting specifications.  Always wear eye protection and follow all under car safety precautions.  Serious injury or death could occur if safety measures are not followed.